## Slide 1: 3GPP TR 36.885 v14.0.0 3rd Generation Partnership Project; Technical Specification Group Radio Access Network; Study on LTE-based V2X Services; (Release 14) PC5-based V2V, V2I Channel model Urban case
September. 15. 2021
Donghee Han
dhh0425@sogang.ac.kr

## Slide 2: Contents
Terminology
시나리오 및 하이퍼 파라미터 값 선정
생성 순서도
순서도 별 참고 테이블(하이퍼 파라미터) 및 공식
테이블 공식에 따라 적용하여 생성했을때 값 및 그래프
최종 데이터 및 그래프
향후 응용 방법(V2V DQN 논문)
Development Environment
Reference

## Slide 3: Symbols
■ PC5 : 이동 핸드세트가 무선 채널을 통해 다른 UE와 직접 통신하는 인터페이스.
(C-V2X에서 PC5 인터페이스는 V2V 및 V2I의 직접 통신으로 사용.)

## Slide 4: 시나리오 및 하이퍼 파라미터 값 선정
Parameter |  | Assumption
Carrier frequency |  | - PC5 based V2V : 6 GHz, 2 GHz - V2I : 6GHz (Baseline) for UE type (RSU), 2GHz for eNB type RSU
Bandwidth |  | - PC5 based V2V : 10 MHz - V2I : 10MHz for UE type RSU, 10MHz for each of Down link and Up link in FDD, 20MHz in TDD for eNB type RSU - V2P : 10 MHz is baseline
Number of carriers |  | - One carrier is baseline
Vehicle UE, UE type RSU, Pedestrain UE paraters | Antenna height | -1.5m for vehicle UE and pedestrain UE - 5 m for UE type RSU
 | Antenna gain | - 3 dBi for vehicle UE and UE type RSU - 0 dBi for pedestrain UI
 | Antenna pattern | Omni 2D
 | Maximum transmit power | 23 dBm
 | Noise figure | 9 dB
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p62
Table A.1.1-1: Details of evaluation scenarios

## Slide 5: 생성 Block diagram(Urban case)
Create
Road
Drop vehicle, base station
(position)
- Set vehicle state
(direction, velocity...)
- t = 0 Init / t > 0 Update V2V(Vehicle to Vehicle) link
- NxN matrix
- Large scale fading
- Path loss
- Shadowing
- Small scale fading
- Fast fading
- t = 0 Init / t > 0 Update V2I(Vehicle to Infrastructure) link
- 1XN matrix
- Large scale fading
- Path loss
- Shadowing
- Small scale fading
- Fast fading
Update vehicle position based on vehicle state
Vehicle-to-vehicle channels are updated during the simulation as follows:
- Let N be the number of vehicle UE in system simulation
- Initialization (at time 0)
- N vehicle locations are generated per agreed drop model
- PL (0) – NxN matrix generated as per vehicle locations and agreed channel models
- Shadowing (in log domain): S(0) – NxN i.i.d. (with the exception that
shadowing between two vehicles should be the same in the two
directions) normal matrix generated as per agreed shadowing model
- Fading (0) – NxN i.i.d. processes with a common distribution
- Update (at time 100*n ms)
- Vehicle locations are updated as per agreed update rules
- PL(n) – N x N matrix generated as per updated vehicle locations
- S(n) = exp(-D/D_corr) .* S(n-1) +sqrt{ (1-exp(-2*D/D_corr))}.*N_S(n)
- where N_S(n) is an NxN i.i.d. (with the exception that shadowing
between two vehicles should be the same in the two directions)
normal matrix generated as per the agreed shadowing model
- D is the update distance matrix where D(i,j) is change in distance of
link i to j from time n-1 to time n
- Fading process is not impacted due to vehicle location updates
(fading is only updated due to time)
- UE performance should reflect fast fading variation within the subframe
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p68
A.1.4 Channel model

## Slide 6: Create Road
Parameter | Urban case
Number of lanes | 2 in each direction (4 lanes in total in eacy street)
Lane width | 3.5m
Road grid size by the distance beetween intersections | 433m * 250m Note that 3 m is reserved for side walk per direction
Simulation area size | Minimum [1299 m * 750 m]
Vehicle density | Average inter-vehicle distance in the same lane is 2.5 sec * absolute vehicle speed. Baseline: The same density/speed in all the lanes in one simulation.
Absolute vehicle speed | 15 km/h, 60 km/h
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p64
Table A.1.2-1: Details of vehicle UE drop and mobility model

## Slide 7: Create Road(Urban case)
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p64
Figure A.1.2-1:Road configuration for urban case

## Slide 8: Drop vehicle, base station (Urban case)
Vehicle UEs are dropped on the roads according to spatial Poisson process.
Vehicle density is determined by the vehicle speed
macro eNB is 500 m and the wrap around model in
Figure A.1.3-1 is used.
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p65, p66
Figure A.1.3-1 : Wrap around model for urban case

## Slide 9: Set vehicle UE’s state
Vehicle No. | Absolute vehicle speed
0 | 15 km/h or 60 km/h
1 | 15 km/h or 60 km/h
... | 15 km/h or 60 km/h
N | 15 km/h or 60 km/h
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p64
Table A.1.2-1: Details of vehicle UE drop and mobility model

## Slide 10: Set vehicle UE’s state
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p64
Table A.1.2-1: Details of vehicle UE drop and mobility model

## Slide 11: Initialize V2V(Vehicle to Vehicle) link
N ：Number of vehicles
R : Number of Resource block
1. Large scale fading
- Shadow fading (NxN matrix)
- Pathloss (NxN matrix)
2. Small scale fading
- Fast fading (NxNxR matrix)
No. 0
No. 1
No. 2
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p64
Table A.1.2-1: Details of vehicle UE drop and mobility model

## Slide 12: Initialize V2V(Vehicle to Vehicle) link
3GPP 36.885
Release 14
WINNER+ B1
Manhattan grid layout
Notes: 3GPP TR 36.885 V14.0.0 (2016-06) p7 Table A.1.4-1: Assumptions for vehicle-to-vehicle channel
WINNER II channel models (Febuary 2008) Page 44 Table 4-4 Summary table of the path-loss models

## Slide 13: Initialize V2V(Vehicle to Vehicle) link
Large scale fading(N : Number of vehicles )
- Shadow fading (NxN matrix)
Notes: WINNER II channel models (Febuary 2008) Page 44 Table 4-4 Summary table of the path-loss models

## Slide 14: Initialize V2V(Vehicle to Vehicle) link
Large scale fading(N : Number of vehicles )
- Pathloss model (NxN matrix)
Notes: WINNER II channel models (Febuary 2008) Page 44 Table 4-4 Summary table of the path-loss models

## Slide 15: Initialize V2V(Vehicle to Vehicle) link
Small scale fading(N : Number of vehicles , R : Resource block )
- Fast fading (NxNxR matrix)
(Fast fading은 position의 영향을 받지 않음.)
Notes: 3GPP TR 36.843 V12.0.1 (2014-03)
DDPG-Based Resource Allocation Scheme for NOMA Vehicular Communications 논문 : Fast fading을 Reyleigh fading을 사용.
Deep Reinforcement Learning Based Resource Allocation for V2V Communications 논문 : 실수부와 허수부를 독립적으로 가우시안 distrubution을 사용.
Reyleigh fading WIKI : https://ko.wikipedia.org/wiki/%EB%A0%88%EC%9D%BC%EB%A6%AC_%ED%8E%98%EC%9D%B4%EB%94%A9

## Slide 16: Initialize V2V(Vehicle to Vehicle) link
Small scale fading(N : Number of vehicles , R : Resource block )
Fast fading method
1. Deep Reinforcement Learning Based Resource Allocation for V2V Commnunications 논문
-> Gaussian distrubution method
2. DDPG-Based Resource Allocation Scheme for NOMA Vehicular Communications 논문
-> Reyleigh fading method
Notes: 3GPP TR 36.843 V12.0.1 (2014-03)
DDPG-Based Resource Allocation Scheme for NOMA Vehicular Communications 논문 : Fast fading을 Reyleigh fading을 사용.
Deep Reinforcement Learning Based Resource Allocation for V2V Communications 논문 : 실수부와 허수부를 독립적으로 가우시안 distrubution을 사용.
Reyleigh fading WIKI : https://ko.wikipedia.org/wiki/%EB%A0%88%EC%9D%BC%EB%A6%AC_%ED%8E%98%EC%9D%B4%EB%94%A9

## Slide 17: Overall V2V(Vehicle to Vehicle) link
Number of vehicles : 3
Resource block: 3
No. 0
No. 1
No. 2
Notes: 3GPP TR 36.843 V12.0.1 (2014-03)
DDPG-Based Resource Allocation Scheme for NOMA Vehicular Communications 논문 : Fast fading을 Reyleigh fading을 사용.
Deep Reinforcement Learning Based Resource Allocation for V2V Communications 논문 : 실수부와 허수부를 독립적으로 가우시안 distrubution을 사용.
Reyleigh fading WIKI : https://ko.wikipedia.org/wiki/%EB%A0%88%EC%9D%BC%EB%A6%AC_%ED%8E%98%EC%9D%B4%EB%94%A9

## Slide 18: Initialize V2I(Vehicle to Infrastructure) link
No. 0
No. 1
No. 2
N ：Number of vehicles
R : Number of Resource block
1. Large scale fading
- Shadow fading (N matrix)
- Pathloss (N matrix)
2. Small scale fading
- Fast fading (NxR matrix)
Notes: 3GPP TR 36.843 V12.0.1 (2014-03)
DDPG-Based Resource Allocation Scheme for NOMA Vehicular Communications 논문 : Fast fading을 Reyleigh fading을 사용.
Deep Reinforcement Learning Based Resource Allocation for V2V Communications 논문 : 실수부와 허수부를 독립적으로 가우시안 distrubution을 사용.
Reyleigh fading WIKI : https://ko.wikipedia.org/wiki/%EB%A0%88%EC%9D%BC%EB%A6%AC_%ED%8E%98%EC%9D%B4%EB%94%A9

## Slide 19: Initialize V2I(Vehicle to Infrastructure) link
Notes: 3GPP TR 36.843 V12.0.1 (2014-03) Table A.1.4-2

## Slide 20: Initialize V2I(Vehicle to Infrastructure) link
Large scale fading(N :차량의 수 )
- Shadow fading (N matrix)
Notes: 3GPP TR 36.843 V12.0.1 (2014-03) Table A.1.4-2

## Slide 21: Initialize V2I(Vehicle to Infrastructure) link
Large scale fading(N :차량의 수 )
- Pathloss model (N matrix)
Notes: WINNER II channel models (Febuary 2008) Page 44 Table 4-4 Summary table of the path-loss models

## Slide 22: Initialize V2I(Vehicle to Infrastructure) link
Small scale fading(N :차량의 수,R : Resource block )
- Fast fading (NxR matrix)
(Fast fading은 position의 영향을 받지 않음.)
1. Deep Reinforcement Learning Based Resource Allocation for V2V Commnunications 논문
-> Gaussian distrubution method(V2V Link와 동일한 계산 공식)
2. DDPG-Based Resource Allocation Scheme for NOMA Vehicular Communications 논문
-> Reyleigh fading method(V2V Link와 동일한 계산 공식)
Notes: WINNER II channel models (Febuary 2008) Page 44 Table 4-4 Summary table of the path-loss models

## Slide 23: Overall V2I(Vehicle to Infrastructure) link
No. 0
No. 1
No. 2
Number of vehicles : 3
Resource block: 3
eNodeB : 1

## Slide 24: Update(time step 100ms)
3 차량, 1 eNodeB
No. 0
No. 1
No. 2
t0
t1
No. 0
No. 1
No. 2
100ms

## Slide 25: Update(time step 100ms)
V2V link , V2I link
- Pathloss matrix update
V2V, V2I link에 Initialize 공식
- Fast fading matrix
V2V, V2I link에 Initialize 공식
Notes: 3GPP TR 36.885 V14.0.0 (2016-06)

## Slide 26: Update(time step 100ms)
V2V link Shadowing matrix
V2I link Shadowing matrix
Notes: 3GPP TR 36.885 V14.0.0 (2016-06)

## Slide 27: ANALYSYS
Notes: 3GPP TR 36.885 V14.0.0 (2016-06)

## Slide 28: Development Environment
Win10 Pro x64
Anaconda
Python 3.7.3 Version
Pytorch 1.8.0
Pandas 1.2.3
Matplotlib 3.3.4
Numpy 1.19.2

## Slide 29: Reference
[1] Neural Networks and Deep Learning, Charu C. Aggarwal
[2] Throughput Analysis of Proportional Fair Scheduling, Jaewoo So, Senior Member, IEEE
[3] 밑바닥 부터 시작하는 딥러닝, 사이토 고키, 한빛미디어
[4] PyTorch를 활용한 강화학습/심층강화학습 실전 입문, 오가와 유타로, 위키북스
[5] Logistic Regression, http://hleecaster.com/ml-logistic-regression-concept/
[6] How to Choose Loss Functions When Training Deep Learning Neural Networks
, https://machinelearningmastery.com/how-to-choose-loss-functions-when-training-deep-learning-neural-networks/
[7] Probability Density Functions (PDFs) and Cumulative Distribution Functions (CDFs) for Continuous Random Variables, https://stats.libretexts.org/Courses/Saint_Mary's_College_Notre_Dame/MATH_345__-_Probability_(Kuter)/4%3A_Continuous_Random_Variables/4.1%3A_Probability_Density_Functions_(PDFs)_and_Cumulative_Distribution_Functions_(CDFs)_for_Continuous_Random_Variables